## Slide 1: Cegal in-person Krafthack 2022

## Slide 2: Content
3 4 5 6 9 10 13
Problem Exploration and prepping Model – data exploration Model – considerations Production Dashboard Scalability and transferability

## Slide 3: Problem
Prediction data in dataset from sensors
Predict the future tensile values of the 6 bolts with sensors

## Slide 4: Exploration and prepping
Removing extreme values
Splitting startup and production data
Removed columns of vibration values because of lacking data
Missing values handled by

## Slide 5: Model – Data Exploration
Interesting findings
  Modes: start and operation
    Since power regulations effect data, a new mode called regulations was added
  Changing temperature due to seasons
  Some data is less influential
    Reactive Power
    Turbine rotational speed (constant)
    Vibrations(constant) – should be explored in the future
  Dataset augmentation by splitting into three categories
    Mode, range, ranges in power changes(in operation)
Guide vane opening in three modes
operation
regulation
start

## Slide 6: Model - Considerations
Used three models with random forest regressor
  Random forest = ensemble estimator that fits a number of regression decision trees on various sub-samples of the dataset, and uses averaging to improve the predictive accuracy and control over-fitting
  Adjustable hyperparameters
    n_estimators = number of trees in the forest
    max_features = max number of features considered for splitting a node
    max_depth = max number of levels in each decision tree
    min_samples_split = min number of data points placed in a node before the node is split
    min_samples_leaf = min number of data points allowed in a leaf node

## Slide 7: Model - Considerations
An ensemble model was used since it’s a shotgun approach where weak single regressors can be powerful together.
In training the model we used a 0.33/0.67 test/train split that gave a good result without cross-validation.
operation
regulation
start
Prediction for each mode plotted against the test-values of Bolt1 tension

## Slide 8: Model - Considerations
While the “prediction_input.parquet” file did not have torsion or temperature data included, the model accuracy has decreased to mean RMSE = 21.14
operation
regulation
start

## Slide 9: Production
Updating the model – retrain
Publishing to Azure
CSV file to PowerApps
Dashboard notifying maintainers about predictive values

## Slide 13: Scalability and transferability
Other applications:
  Estimate max power production based on weather conditions and season
  Sub-sea installations
  Oil rig installations
  Maintenance of elevators
  Cars service interval
  Stock prices
  Train maintenance